## Slide 1: Three weeks later: the road-ahead list became a release
ADDENDUM — SHIPPED SINCE THESE SLIDES WERE SUBMITTED (JULY 19)
v1.1.8 — released August 3
▪
Observation presets: one pick — “Pulsar: L-band” — sets every science-critical parameter to the validated geometry; a live readout shows time resolution, DM smearing, disk rate.
Recording integrity: dropped-sample gaps measured from radio timestamps and zero-padded exactly, live — the 28σ gap-repair lesson, now automatic (verified: 0 samples lost at 16 MS/s).
Automatic post-processing: recording stops → PRESTO runs → a self-contained PDF: fold chart, commands, numbers, and a plain-language verdict (incl. “that’s terrestrial, not a pulsar”).
ezRA drift-scan format: the same app writes ezCol-compatible files for Ted Cline’s ezRA suite — the DSES 60-ft dish is doing hydrogen-line drift scans with it today.
▪
True hardware sample rates: B210 to its real 61.44 MS/s ceiling, master-clock-clean presets.
v1.2.0 — landed this morning
Full UI redesign: menus, six dockable panels, one-click observation setup — ask during Q&A and I’ll show it live.